## Slide 1: HDMI to VGA Converter
Naoaki Takatsu
CECS 461
May 14, 2019

## Slide 2: Features
Supports HDMI display resolution of:
640x480, 800x600, 1280x720, 1280x1024, and1920x1080
Print color bar test screen to cover up display
Color inverting screenshot
Stop/resume streaming
Frame rate of 60 FPS

## Slide 3: Materials needed
Zybo board
Micro USB to USB cable
HDMI cable
VGA cable
HDMI source
VGA output device

## Slide 4: Operation
Push Button | Menu
0 | Pause/resume stream
1 | Capture frame and invert color/resume stream with original color
2 | Change display resolution with respect to dip switch value
3 | Display/hide color bar test screen to hide stream
Dip Switch Value | HDMI Resolution
1 | 640x480
2 | 800x600
3 | 1280x720
4 | 1280x1024
5 | 1920x1080
0 | No change
Other | Display error message
1. Establish UART connection and open serial terminal.
2. Program FPGA to Zybo board and run the software application as GDB in Xilinx SDK.
3. Connect HDMI and VGA cables respectively from source to board.
4. View serial terminal for available options and press respective button to execute one of the following:
5. Enter one of the following dip switch values to change the HDMI display resolution:

## Slide 5
Software flowchart
For initialization and push button

## Slide 6
Software flowchart
For Dip switch

## Slide 7
Hardware Block Diagram
Convert HDMI to RGB Data
Pass RGB Data as AXI4 Stream Data
Control Video Timing for HDMI
Control Video Timing Dynamically
Control Video Timing for VGA
Pass AXI4 Stream Data as RGB Data
Concatenate Interrupt Requests
Dip Switch
Push Button
Pass RGB Data as VGA Output
Hotplug for HDMI
HDMI Output Enable
Save Video Frames to Internal Memory

## Slide 8
Dvi to rgb video decoder Block
TMDS – Transition-Minimized Differential Signaling, DVI/HDMI data input
DDC – Display Data Channel, provides digital communication between computer display and graphics adapter
RGB – Red Green Blue, Pixel Data including color and timing data

## Slide 9
Video In to axi4-stream Block
vid_io_in – RGB display and timing data input
video_out – video display output
vtiming_out – video timing output

## Slide 10
Video Timing controller (HDMI) block
ctrl – s_axi data
vtiming_in – video timing input
irq – interrupt request signal

## Slide 11
Video Timing controller (VGA) block
ctrl – s_axi data
vtiming_out – video timing output
irq – interrupt request signal

## Slide 12
Axi4-stream to video out block
video_in – input display data from AXI interconnect
vtiming_in – input timing data from VGA timing block
vid_io_out – converted RGB data output

## Slide 13
RGB to vga output block
vid_in – Converted RGB data
PixelClk – pixel clock input from dynamic clock generator
Vga_pXX – VGA color and timing output data

## Slide 14
Dynamic clock generator block
s00_axi – AXI interface pin
PXL_CLK_O – pixel clock output for VGA

## Slide 15
Source Codes

## Slide 16
Source Codes

## Slide 17
Source Codes

## Slide 18
Source Codes

## Slide 19
Source Codes

## Slide 20
VGA Timing

## Slide 21: Working Project

## Slide 22: Error
When attempting to run GDB on SDK from Vivado 2016.4, the error shown on the right has always showed up
This error has caused me to transition my project from Vivado 2016.4 to 2018.3 and vice-versa multitude of times

## Slide 23: Stuck between a rock and a hard place
The HDMI input demo on the Digilent website is meant to be built on Vivado 2016.4 edition
However, due to the previously stated error, I needed to download the 2018.3 edition HDMI input project from the forums
The project works fine, but the console outputs tons of error due to outdated BSP
In addition to that, all modifications made on the application software were ignored upon running with GDB
After recompiling the whole hardware in Vivado, creating a brand new BSP, and replicating original C code on the application software, all the error messages have disappeared
Despite of having no more error messages, now the HDMI feed wasn’t being displayed on the monitor
Looking through tons of HDMI references, assuming that the issue was on either the hardware or software side, has given me a good amount of sleepless nights

## Slide 24: Error solved!
After spending days of trial and error, debugging, and researching, I have finally managed to find a forum with a working solution
The error was caused due to missing “-force” option in the Vivado 2016.4 edition
Simply downloading and replacing the xmdterm.tcl in the SDK installation folder has solve this problem

## Slide 25: Future plans
Continue streaming while color filter is turned on
Take screenshot/footage and save it to micro SD card
Pull HDMI audio source to headphone jack

## Slide 26: References
-Digilent forums
-Tutorial: How to start a video processing application with Vivado VHDL
-Video Processing Using VHDL and ZYBO Board
-tinyvga.com/vga-timing
-http://marsee101.blog19.fc2.com

## Slide 27: Thank you